## Slide 1: CS144 An Introduction to Computer Networks
Packet Switching
Queue models
Nick McKeown
Professor of Electrical Engineering
and Computer Science, Stanford University

## Slide 2: Outline
Simple deterministic queue model
Small packets reduce end to end delay
Statistical multiplexing

## Slide 3: Simple model of a router queue
Properties of A(t), D(t):
A(t), D(t) are non-decreasing
A(t) >= D(t)
R
A(t), l
D(t)
Router queue
Q(t)
HIDE
Notes: DRAW the next 3 slides to explain simple model of a router queue to simple deterministic model of a queue (3,4,5).

## Slide 4: Simple model of a router queue
Notes: DRAW the next 3 slides to explain simple model of a router queue to simple deterministic model of a queue (3,4,5).

## Slide 5: Simple model of a queue
A(t)
D(t)
Cumulative number of bytes departed up until time t.
time
Link
rate
Cumulative
number of bytes
Cumulative number of bytes arrived up until time t.
R
A(t)
D(t)
Q(t)
Properties of A(t), D(t):
A(t), D(t) are non-decreasing
A(t) >= D(t)
R
HIDE

## Slide 6: Simple model of a queue
A(t)
D(t)
Cumulative number of bytes departed up until time t.
Link
rate
Cumulative number of bytes arrived up until time t.
Q(t)
R

## Slide 7: Simple model of a queue
D(t)
A(t)
Time
Q(t)
d(t)
Queue occupancy: Q(t) = A(t) - D(t).
Queueing delay, d(t), is the time spent in the queue by a byte that arrived at time t, assuming the queue is served first-come-first-served (FCFS).
Cumulative
number of bytes
HIDE

## Slide 8: Simple model of a queue

## Slide 9: Example
Cumulative
number of bits
Every second, a 100 bit packet arrives to a queue at rate 1000b/s. The maximum departure rate is 500b/s. What is the average occupancy of the queue?
D(t)
A(t)
time
0.1s
0.2s
1.0s
100
Solution: During each repeating 1s cycle, the queue fills at rate 500b/s for 0.1s, then drains at rate 500b/s for 0.1s. Over the first 0.2s, the average queue occupancy is therefore bits.
The queue is empty for 0.8s every cycle, and so average queue occupancy:

## Slide 10: Outline
Simple deterministic queue model
Small packets reduce end to end delay
Statistical multiplexing

## Slide 11: Packet Switching Why not send the entire message in one packet?
Breaking message into packets allows parallel transmission across all links, reducing end to end latency.
R1
R2
R3
p/r1
R1
R2
R3
M/r1
A
B

## Slide 12: Outline
Simple deterministic queue model
Small packets reduce end to end delay
Statistical multiplexing

## Slide 13: Statistical Multiplexing Basic idea
time
time
Two flows
Average rate
Many flows
Average rates of: 1, 2, 10, 100, 1000 flows.
rate
rate
time
rate
One flow
Notes: Real traffic is not usually DETERMINISTIC --- packets show up at random times.
Network traffic is bursty. i.e. the rate changes frequently.
Peaks from independent flows generally occur at different times.
Conclusion: The more flows we have, the smoother the traffic.
This is what is known as STATISTICAL MULTIPLEXING, and is one of the main reasons packet switching is used.
The basic idea is that the link capacity we need to carry N flows, is much less than N times the capacity we need to carry 1 flow.

## Slide 14: Packet Switching Statistical Multiplexing
Link rate, R
X(t)
Queue Length
X(t)
Time
Packet buffer
Packets for one output
Data
Hdr
Data
Hdr
Data
Hdr
R
R
R
Because the buffer absorbs temporary bursts, the egress link need not operate at rate N.R.
But the buffer has finite size, B, so losses will occur.
1
2
N
HIDE

## Slide 15: Packet Switching Statistical Multiplexing
Link rate, R
Q(t)
Packet buffer
Packets for one output
Data
Hdr
Data
Hdr
Data
Hdr
R
R
R
Statistical multiplexing means the egress link need not run at rate NR.
The buffer absorbs brief periods when the aggregate rate exceeds R.
Because the buffer has finite size losses can occur.
1
2
N
Notes: DRAW in the graph from the previous slide showing X(t) [queue occupancy] growing.
DRAW the value of B, to show that packets will be dropped when X(t) reaches B.

## Slide 16: Statistical Multiplexing
B
A
time
time
Rate
Rate
C
C
A
C
B
C
Notes: Statistical multiplexing
  Important if traffic is bursty
Less expensive
Contention requires buffering
  Variable delay => no QoS guarantees

## Slide 17: Statistical Multiplexing Gain
A
B
R
2C
R < 2C
A+B
time
Rate
Statistical multiplexing gain = 2C/R
Notes: Statistical multiplexing
  Important if traffic is bursty
Alternative definition: For a given buffer size, the ratio of the rates needed to prevent packet loss. The bigger the buffer, the bigger a temporary surge can be accommodated, and hence the bigger the statistical multiplexing gain.

## Slide 18: Summary
Often, we can use a simple deterministic model of a queue to understand the packet dynamics in a network.
We break messages into packets because it lets us pipeline the transfer, and reduce end to end delay.
Statistical multiplexing lets us carry many flows efficiently on a single link.

## Slide 19: <end>